## Slide 1: Transport Layer (TCP)
Lecture 5 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: Objectives
TCP Header
TCP Services

## Slide 3
TCP Segment Header

## Slide 4: Byte Number
The bytes of data being transferred in each connection are numbered by TCP.
The numbering starts with an arbitrarily generated number.
An arbitrary number between 0 and 232 − 1 for the number of the first byte.
For example if the number of the first byte happens to be 1067 and the total data to be sent is 3000 bytes .
What is the byte number for the first byte of data and last byte of data?
First Byte Number
1067
Last Byte Number
4066

## Slide 5: Sequence Numbers
The sequence number of the first segment is the ISN (initial sequence number), which is a random number (byte number).
The sequence number of any other segment is the sequence number of the previous segment plus the number of bytes (real or imaginary) carried by the previous segment.
Suppose a TCP connection is transferring a file of 5,000 bytes. The first byte is numbered 10,001. What are the sequence numbers for each segment if data are sent in five segments, each carrying 1,000 bytes?
Solution:

## Slide 6: Acknowledgement Number
If receiving host TCP receives uncorrupted data, then…
It is acknowledged using the acknowledgement number
The value of the acknowledgment field in a segment defines the number of the next byte the receiver expects to receive.
For example if the sender receives 1001 as the acknowledgement number.
What does it mean?
Received all data up to
1000, tells the sender that it ready to receive the next data from 1001 byte number.
Note :This does not indicate receiver has received 1000 bytes of data.

## Slide 7
Expectational Acknowledgement
Acknowledgement Number

## Slide 8: Acknowledgement Number
The acknowledgment number is cumulative.
Receiver acknowledges multiple data segments in one acknowledgement.
Sender
Receiver

## Slide 9: Header Length
Header Length :
  Indicates the number of 4-byte words
  The length of the header can be between 20 and 60 bytes

## Slide 10: Control Bits
Control Bits:
  This field defines 6 different control bits or flags
  One or more of these bits can be set at a time
  These bits help indicate connection establishment and termination, flow control

## Slide 11: Window Size
Window Size:
  This field defines size of data in bytes of the sending TCP process
  The maximum size of the window is 65,535 bytes
  Normally referred to as the receiving window (rwnd )
  The sender must obey the dictation of the receiver in this case

## Slide 12: Checksum
This 16 bits field is used to detect errors (i.e., flipped bits) in the transmitted segment (intentionally or unintentionally) while traveling through the network.
Also present in UDP header
Mandatory in TCP but not in UDP
Process is same for both protocols
TCP/UDP Header
TCP/UDP Body
Pseudo IP Header
UDP HEADER

## Slide 13: Checksum
Transmitted: 5 6 11
Received: 4 6 11
1st number
2nd number
sum
receiver-computed
checksum
sender-computed
checksum (as received)
=
UDP HEADER

## Slide 14: Checksum Process
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  Not equal - error detected
  Equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment

## Slide 15: Checksum: an example
example: add two 16-bit integers
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1

## Slide 16: Checksum: weak protection!
example: add two 16-bit integers
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!

## Slide 17: Urgent Pointer
This 16-bit field, which is valid only if the urgent flag is set.
Used when the segment contains urgent data.
It defines a value that must be added to the sequence number to obtain the number of the last urgent byte in the data section of the segment.
1500
1500
1oo1

## Slide 18: Options
  There can be up to 40 bytes of optional information in the TCP header
  Provides a way to deal with limitations of the original header
  For example :
    MSS (Maximum Segment Size) is defined as the largest block of data that a sender using TCP will send to the receiver

## Slide 19: Functions of the Transport Layer
Primary responsibilities:
  Segmenting the data and managing each piece.
  Reassembling the segments into streams of application data.
  Identifying the different applications.
  Multiplexing
  Establishing and terminating a connection.
  Enabling error control and recovery.
  Performing flow control between end users.
Only TCP
UDP &TCP

## Slide 20: Function 6 Connection Establishment and Termination for Reliability

## Slide 21: Connection Establishment
TCP sets up a connection between end hosts before sending data
This process is known as ”Three-way handshake”
After the connection is established the hosts can send data

## Slide 22
Source Port No. |  |  |  |  |  | Destination Port No. | 
Sequence No. |  |  |  |  |  |  | 
Acknowledgement No. |  |  |  |  |  |  | 
 | U | A | P | R | S | F | Window Size
Others |  |  |  |  |  |  | 
80
49152
Others |  |  |  |  |  |  | 
49152
80
100
0
S
80
49152
0
101
S
A
80
49152
101
1
A
3 Way Handshake : Connection Establishment
4000 Bytes
8000 Bytes

## Slide 23
3 Way Handshake : Connection Establishment

## Slide 24
Data Transfer

## Slide 25
Data Transfer Continued..

## Slide 26
Source Port No. |  |  |  |  |  | Destination Port No. | 
Sequence No. |  |  |  |  |  |  | 
Acknowledgement No. |  |  |  |  |  |  | 
 | U | A | P | R | S | F | Window Size
Others |  |  |  |  |  |  | 
80
49152
Others |  |  |  |  |  |  | 
49152
80
10001
17001
80
49152
10002
F
17001
A
3 Way Handshake : Connection Termination
4000 Bytes
8000 Bytes
10002
17002

## Slide 27: Connection Termination :: Half Close

## Slide 28: Function 6 Error Control and Recovery for Reliability

## Slide 29: Reliability in TCP
TCP provides reliability using error control
Error control includes mechanisms for
  detecting and resending corrupted segments
  resending lost segments
  storing out-of order segments until missing segments arrive
  detecting and discarding duplicated segments.
Error control in TCP is achieved through
  Checksum
  Acknowledgment
  Time-out and retransmission

## Slide 30: Error Control
Checksum
  Each segment includes a checksum field, which is used to check for a corrupted segment
  If a segment is corrupted, as detected by an invalid checksum, the segment is discarded
Acknowledgment
  Using Acknowledgement Number to confirm the receipt of data segments.
  To confirm control segments that carry no data, but consume a sequence number
  ACK segments do not consume sequence numbers and are not acknowledged.

## Slide 31
Retransmission
When a segment is sent, it is stored in a queue until it is acknowledged.
Retransmission of segment will occur
  After Retransmission Time Out
  The sending TCP maintains one retransmission time-out (RTO) timer for each connection.
  When the timer matures TCP resends the segment in the front of the queue if the segment is not acknowledged
After Three Duplicate ACK Segments
  To be explained later
Error Control

## Slide 32
Seq – 1201
Ack – 4001 [Data 200 bytes]
Seq – 4001
Ack – 1401 [Data 1000 bytes]
Seq – 1201
Ack – 5001
Seq – 4001
Ack - 1401 [Data 1000 bytes]
Seq – 4001
Ack- 1401 [Data 1000 bytes]
Time Out
500 ms
Start
> 500 ms
Stop
Seq – 1201
Ack - 7001
Normal Operation
Start
Start

## Slide 33
Segment Lost or Corrupted?
Retransmission of segment ??
How will the sender know ??
What about the receiver, not aware of a packet sent?
RTO - Retransmission after time out.
Other Scenarios

## Slide 34
Seq – 7001
Ack – 1401 [Data 1000 bytes]
Seq – 8001
Ack - 1401 [Data 1000 bytes]
Seq – 9001
Ack- 1401 [Data 1000 bytes]
Time Out
Start
< 500 ms
Stop
Seq – 1401
Ack - 9001
Seq – 1401
Ack - 9001
Buffer
Seq – 9001
Ack – 1401 [Data 1000 bytes]
Seq – 10001
Ack - 1401 [Data 1000 bytes]
Time out & Restart Timer
Seq – 1401
Ack - 11001
Buffer
Stop
Buffer
Start
Lost Segment

## Slide 35: Out of Order Segments
TCP implementations today do not discard out-of-order segments.
They store them temporarily .
Flag them as out-of-order segments until the missing segments arrive.
Out-of-order segments are never delivered to the process.
TCP guarantees that data are delivered to the process in order.

## Slide 36
Seq – 11001
Ack – 1401 [Data 1000 bytes]
Seq – 12001
Ack- 1401 [Data 1000 bytes]
Time Out
Seq – 1401
Ack - 12001
Seq – 1401
Ack - 12001
Seq – 11001
Ack – 1401 [Data 1000 bytes]
Time out & Restart Timer
Buffer
Time Out Timer
Buffer
Start
Stop
Seq – 13001
Ack- 1401 [Data 1000 bytes]
Seq – 14001
Ack- 1401 [Data 1000 bytes]
Seq – 15001
Ack- 1401 [Data 1000 bytes]
Seq – 9001
Ack- 1401 [Data 1000 bytes]
Seq – 1401
Ack - 12001
Seq – 1401
Ack - 12001
Seq – 1401
Ack - 12001
Seq – 1401
Ack - 12001
Start
Seq – 12001
Ack- 1401 [Data 1000 bytes]
1
2
3
Lost ACK
3 ACKs – Fast Transmission

## Slide 37: Function 7 : Flow Control and Recovery for Reliability

## Slide 38: Flow Control
Transmission Control Protocol (TCP) uses a sliding window for flow control.
What is the “Window ”?
  Indicates the size of the device's receive buffer for the particular connection.
  How much data a device can handle from its peer at one time before it is passed to the application process.
  Set by receiver of data
  Example : The server's window size was 360. This means the receiver is willing to take no more than 360 bytes at a time from the sender.

## Slide 39
. . . | 200 | 201 | . . . . . | 260 | 261 | . . . . . | 300 | 301 | . . .
Bytes that are acknowledged
Window Size = 100 bytes
Window Size as advertised by the receiver
Variables
Sf = 201
Sn = 261
Outstanding Bytes
sent but not acknowledged
First outstanding byte
Next byte to send
Sf
Sn
Bytes that cannot be sent
Bytes that can be sent (Usable window)
Sender Sliding Window

## Slide 40
Sliding of Sender Window

## Slide 41
. . . | 200 | 201 | . . . | 241 | 242 | . . . | 260 | 261 | . . . . . | 300 | 301 | . . .
Window Size = 100 bytes
Window Size as advertised by the receiver
Variables
Sf = 201
Sn = 261
Outstanding Bytes
sent but not acknowledged
First outstanding byte
Sf
Next byte to send
Sn
Bytes that cannot be sent
Bytes that can be sent (Usable window)
Bytes that are acknowledged
#Sender receives a segment with ACK 241
And rwnd = 60
First outstanding byte
Sf
Bytes that are acknowledged
Outstanding Bytes
sent but not acknowledged
340
rwnd = 100
Sliding of Sender Window
Variables
Sf = 241
Sn = 261

## Slide 42
. . . | 200 | 201 | . . . . . | 260 | 261 | . . . . . | 300 | 301 | . . .
Bytes that have already been pulled by the process
rwnd= buffer size – number of bytes to be pulled
Receive window and allocated buffer
Bytes received and acknowledged, waiting to be consumed by process
Next byte to be pulled by process
Next byte expected to receive
Rn
Bytes that cannot be received
Bytes that can be received from the sender
Receive window(rwnd)
Receiver Sliding Window
Window Size = 100 bytes
= 40 bytes

## Slide 43
Sliding of Receiver Window

## Slide 44: Flow Control Example

## Slide 45: Flow Control Example Contd

## Slide 46: Different TCP Sliding Window Protocols
Selective Repeat Protocol
  Only those segments are re-transmitted which are found lost or corrupted
  Keep track of out of order segments at the receiver side
  More efficient for noisy channels
  Widely used in TCP

## Slide 47
Seq – 7001
Ack – 1401 [Data 1000 bytes]
Seq – 8001
Ack - 1401 [Data 1000 bytes]
Seq – 9001
Ack- 1401 [Data 1000 bytes]
Time Out
Start
< 500 ms
Stop
Seq – 1401
Ack - 9001
Seq – 1401
Ack - 9001
Buffer
Seq – 9001
Ack – 1401 [Data 1000 bytes]
Seq – 10001
Ack - 1401 [Data 1000 bytes]
Time out & Restart Timer
Seq – 1401
Ack - 11001
Buffer
Stop
Buffer
Start
Go Back N ARQ
Seq – 10001
Ack - 1401 [Data 1000 bytes]

## Slide 48: Different TCP Sliding Window Protocols
Go Back N Protocol
  If the sent segment are are found corrupted or lost then all the segments are re-transmitted from the lost segment to the last segment transmitted
  Do not keep track of out of order segments
  Efficient for less noisy channel

## Slide 49: Overall Flow control
The initial window size is agreed during the three-way handshake.
If this is too much for the receiver and it loses data (e.g. buffer overflow) then it can decrease the window size.
If all is well then the receiver will increase the window size.

## Slide 50: The End